## Slide 1
21st Century Truck TARDEC Fall Meeting
Active Safety Systems - Road to Autonomous Functionality
Alan Korn
Director-Advanced Brake System Integration
November 6, 2013

## Slide 2: Presentation Overview
Meritor WABCO Background
Heavy Truck Crash Facts
NHTSA Automation Classifications
Today’s Active Safety System Technology
  ABS, Stability Control, Collision Mitigation, LDW,
Future Active Safety System Technologies
  Advanced CMS, Driver/Vehicle Performance Management, V2V, CACC
  Increased automation
11/06/13

## Slide 3
Safety Strong
Efficiency Smart
A leader in Advanced Integrated Safety Systems
Focused on improving performance and handling, assisting the driver in maintaining control of the vehicle and avoiding accidents
Continued commitment to safety systems capable of reducing commercial vehicle accidents
ABS ECU’s
Hydraulic
RSS
RSC
ESC
ESC SMART
CAMERA BASED LANE TRACKING SYSTEM
Driver Alertness Warning
LDW
LONG RANGE RADARS
ACC
FCW
CMS
SAFETY SYSTEM DATA MANAGEMENT
Driver Monitoring
Data Analytics
11/06/13

## Slide 4
Efficiency Smart
Efficient Air Solutions are engineered for optimized performance with less energy consumption.
Intelligent Air System innovations providing:
  Enhanced efficiency, performance and reliability
  Reduced maintenance and operation costs
Reduced product weight providing:
  Increased payload capabilities
  Further fuel savings
AIR DRYERS
•1200 Plus •ECAD •1200 Regen •Twin
AIR COMPRESSORS
Hi Output
Twin
Clutch
SUSPENSION CONTROLS
  ECAS
  Leveling Valves
11/06/13

## Slide 5: 2011 US Large Truck Crash Statistics
287,000 large truck DOT reported crashes
3,608 trucks involved in fatal crashes
3,757 fatalities - 635 truck occupants
  2.2% increase in total fatalities over 2010
  71% combination vehicles
88,000 injuries - 23,000 truck occupants
Fatalities / 100 million miles traveled 1.41 (+10% from 2010)
  45% reduction from 2000
Alcohol involved in 3.0% of large truck fatal crashes
  Alcohol involved in 27% of passenger car fatal crashes
Ref: 32,367 fatalities from all US motor vehicle crashes
  1.5% fatality reduction over 2010
  1.10 Fatalities / 100 million miles traveled
5
11/06/13

## Slide 6: Large Truck Fatal Crashes 2000-2011
11/06/13

## Slide 7: Elements Driving Safety Improvement
Driving Safety
Improvement
11/06/13

## Slide 8: NHTSA Levels of Automation
Level 0: Driver in complete & sole control of vehicle; braking, steering, throttle
Level 1 Function Specific: One or more systems that automatically assists driver with a primary vehicle control function
Level 2 Combined Function: Two or more primary control functions combined to work in unison to relieve driver of control of these functions
Level 3 Limited Self Driving: Enable driver to cede full control under certain conditions. When necessary, system automatically transitions control back to driver
Level 4 Full Self Driving
Today’s well equipped large trucks are at Level 1
11/06/13

## Slide 9: Current Active Safety Systems
System designed to ASSIST driver in maintaining control of vehicle and reducing crash risk
  Driver remains responsible for safe operation of vehicle and ensuring physical limitations are not exceeded
Contains onboard sensors, actuators and intelligent algorithms to enable automatic intervention of one or more of the vehicle’s primary control functions when safety thresholds are exceeded – braking, steering, throttle
Examples include ABS, Stability Control, Collision Mitigation and Lane Departure Warning
11/06/13

## Slide 10: Antilock Braking System (ABS)
Foundation for advanced safety systems
Helps prevent high levels of wheel slip (wheel lock) during braking
  Typically occurs on slippery road surfaces, light vehicle loads, worn tires
  Wheel lock adversely effects vehicle’s lateral stability (jackknife), ability to steer and stopping distances
11/06/13

## Slide 11: Electronic Stability Control
Closely integrated with ABS
Additional sensors, control valves and software required for increased functionality
  Steer angle, pressure sensor, yaw rate, lateral accelerometer, three brake control valves
  Architecture required for CMS
Reduces risk of untripped rollovers
  Excessive speed in turn, rapid changes of direction on high friction surfaces
Reduced risk of loss of control
  Understeer and oversteer conditions typically on lower friction surfaces
11
11/06/13

## Slide 12
COLOR KEY
Primary
Secondary
Park & Emergency
Blended Air
Supply
Electrical Wire
Tractor ABS + Electronic Stability Control (ESC)
11/06/13
12

## Slide 13: Collision Mitigation Braking System (CMS)
Active braking system designed to reduce / mitigate forward collisions
Based on single radar sensor
Collision, stationary and haptic warnings
Adaptive cruise control and ‘always on’ collision mitigation
  Active braking
Integrated w/ABS and stability control
11/06/13

## Slide 14: CMS Intervention Sequence
t0
Object tracked
Avoidance maneuver not possible
time
t2
t3
t4
Engine Torque Limitation
Brake Activation
Potential rear end collision detected
Hard braking required to prevent collision
t1
System Reactions:
Crash prevented or mitigated
Warning Tone and Lamp
Haptic Warning
Collision warning: Haptic (short brake pulse)
FT
MPH
Automatic braking to assist driver in collision mitigation
FT
MPH
Distance Alert: Visual and Audible
FT
MPH
14
11/06/13

## Slide 15
Vision based technology
Detects and classifies lane markers
Tracks and projects lane ahead of truck
Provides audible warnings
  Lane change made without turn signal indicator (rumble strip warning)
  Functions above 40 MPH
Includes Driver Alertness Warning
  Detection of erratic or degraded driving (drowsiness and/or distraction)
  Software solution requires no additional hardware
Automatic calibration and integrated diagnostics to simplify setup and operation
SAE J 1939 critical event messages
Integrated critical event video with manual download capability
800+ Million miles on North American applications
Lane Departure Warning
11/06/13

## Slide 16: Near Term Future Active Safety Systems
Level One Automation
Next Generation ABS, stability control, CMS
Driver/Vehicle Performance Management
Vehicle Communications
  V2V / V2I
  Cooperative ACC Project
Maximize driver performance by providing support technologies that warn and intervene at critical moments
11/06/13

## Slide 17: ESC Smart Technology
Employs vehicle model to predict stable path
Establishes vehicle dynamic characteristics by self learning and adaptation
  System continually adapts to changes in vehicle’s response characteristics
  “Drive it Away” off OEM assembly line
Minimize vehicle validation test requirements
Globally used across all braking platforms
Competitive ESC platform for non standard vehicle configurations
Efficient throughout vehicle life cycle
11/06/13

## Slide 18: CMS Future Roadmap
Continuously upgrading and pioneering innovation to enhance safety
+
Current
2014
2016
Auto alignment
Dual mode radar
Warning on stationary objects
Evasive maneuver check
Partial braking on stationery objects
Full braking capability on moving or stopped objects
Extended brake assist
In-crash braking
Full braking of stationary objects
Sensor fusion
ACC Stop & Go
Brake pre-fill
Autonomous Emergency Braking
11/06/13
Notes: 18

## Slide 19: Driver / Vehicle Performance Management
Using predictive analytics to detect driving maneuvers that increase crash risk
High use of forward and inboard facing video to achieve driving optimization
Documented feedback striving for self improvement
Vehicle monitoring for predictive maintenance
11/06/13

## Slide 20: V2V / V2I Communications
Dynamic wireless exchange of data between vehicles and infrastructure (5.9 GHz DSRC)
All vehicles on public roads broadcast data regarding position, speed and location
  “Here I Am” data messages
Vehicles sense threats with 360 degree awareness
Estimated to address over 75% of unimpaired crash scenarios
System only provides warnings
Provides traffic stream data that must be integrated with current vehicle based active safety systems
  Can not have two systems providing similar warnings
    On-board CMS, Blindspot detection
20
11/06/13

## Slide 21: V2V/V2I Warnings
Forward Collision
Intersection Movement Assist
Blind Spot
Curve Speed
Bridge Height
Hard Braking
11/06/13

## Slide 22: V2V / V2I Safety Pilot
Field test of technology running in Ann Arbor, MI
  Initiated August 2012
Designed to determine effectiveness of technology in reducing crashes and how drivers respond to applications
Approx 3,000 vehicles, 70 trucks
NHTSA recently announced pilot will be extended 6 months until February 2014
11/06/13
GAO recently released a report summarizing V2V status and potential benefits

## Slide 23: Vehicle 2 Vehicle CV Communication Challenges
Trailer presence and length needs to be considered
  How to automatically supply this data to tractor installed devise
Articulated vehicles present additional challenges
  Intersection clearance, lane changes
Security of messages must be assured
Can payback be ensured during the initial years of deployment?
Will regulation be required to achieve adequate penetration rate for payback (light and heavy vehicles)?
Heavy truck regulatory decision scheduled for 2014 (pass cars 2013)
23
11/06/13

## Slide 24: Cooperative Adaptive Cruise Control Project
Federal Highway (FHWA) awarded project in early October to team led by Auburn University
  Peloton, ATRI, Peterbilt, Meritor WABCO
Team will research Partial Automation for two Truck Platooning
  Cooperative Adaptive Cruise Control builds off current Adaptive Cruise Control
  Key technologies include radar, V2V communications, positioning, actuation and Human-Machine Interfaces (transmitting critical information to leading and following drivers)
11/06/13

## Slide 25: Key Research Tasks
Document traffic flow and fuel economy improvement potentials
System robustness
System reaction to passenger car cut-ins and other highway anomalies
How to find similarly equipped vehicles
Responsibilities of lead driver
Return on investment
11/06/13

## Slide 26: Challenges Moving to Advanced Automation Levels
Achieving sufficient technology payback technology
  Especially Levels 2 & 3
Validation requirements
Potential reduction in driver skills
Transition from complete system control back to driver – Level 3
  Will driver be prepared?
Liability concerns
Infrastructure improvements
Mixed vehicle population
11/06/13

## Slide 27: Next Steps in Autonomous Functionality
Adaptive vehicle based safety systems
  Integrating traffic stream, environment & infrastructure information
Continued development in higher performance sensors and actuators, cost optimized for volume production
Higher software reliability levels and tools to validate
Cybersecurity
11/06/13

## Slide 28: Summary
Use of heavy truck active safety systems increasing
  ABS (mandated)
  Stability control – approx 50% of class 8 tractor build
    Notice of Proposed Rulemaking Issued May 2012
  Collision Mitigation – approx 10% of class 8 tractor build
    Rulemaking being seriously considered
Changes in automation level will be evolutionary, not revolutionary
For the near term, active safety systems will assist drivers, not replace them
11/06/13

## Slide 29: Save Lives, Increase Value, Reduce Costs
Cutting edge
Groundbreaking
Inventive
Novel
Trendsetting
“There’s a way to do it better – find it.”
Thomas Edison
29
Alan Korn
Alan.Korn@meritorwabco.com
001 248 435 4498
Thanks!